## Slide 1
CompLaB3D solve loop: where the graph network runs
Model I/O and setup
Flow solver (D3Q19)
Transport solver (D3Q7)
Reaction solver
Mineral solver (VOP)
Load XML configuration
& initialize the simulation conditions
Run flow simulation to steady state
Execute collision step for transport
Abiotic reaction kinetics
Biotic reaction: one rate path per organism
Equilibrium chemistry
Surface reactions on wetted voxels:
precipitation and dissolution
CA biomass expansion
Mineral node update: seal full voxels,
reopen emptied voxels
Pore geometry
changed?
Re-solve steady-state flow field
Yes
No
Streaming step (D3Q7)
& apply boundary conditions
Output save step
reached?
Write output files (VTI)
Yes
No
Max time steps
reached?
No
+ Δt
Yes
End
inside the biotic reaction step, per organism
interchangeable: each takes the local concentrations and
returns a growth rate and the source terms transport needs
compiled kinetics
flux balance analysis (GLPK / COBRApy)
surrogate network
symbolic rate law
graph network
when it is a graph network:
the network was fitted once, offline
per voxel: scale, two rounds, read out
returns a rate for EVERY species, not just growth
the stoichiometry is structure, not something learned

## Slide 2
The reaction network, drawn as a graph
Two reactions and five species. Every edge is one non-zero entry of the stoichiometric matrix, and carries that number as its weight.
R1 CH4 + SO4 → HS + HCO3
R2 HCO3 + Ca → CaCO3
species nodes
reaction nodes
−1
−1
+1
+1
−1
−1
CH4
SO4
HS
HCO3
Ca
R1
R2
the same graph, written as the matrix S
R1 R2 CH4 -1 0 SO4 -1 0 HS +1 0 HCO3 +1 -1 Ca 0 -1
one row per species, one column per reaction; a zero is an edge that is not there
the same object,
written two ways
HCO3 is the node to watch
It is the only species with an edge to both reactions, so it is the only route by which R1 can influence R2. Nothing had to teach the network that carbonate couples methane oxidation to calcite precipitation. The edge is there because the matrix says it is.
species node
reaction node
− 1 the reaction consumes one mole
+ 1 the reaction produces one mole

## Slide 3
One round of message passing, followed on the graph
A round has two halves. Every species speaks into the reactions it takes part in, then every reaction speaks back. Both sums are weighted by the coefficient on the edge.
half 1: species speak into reactions
CH4
SO4
HS
HCO3
Ca
R1
R2
each reaction adds up the states of the species on its edges, each multiplied by that edge's coefficient
half 2: reactions speak back
CH4
SO4
HS
HCO3
Ca
R1
R2
each species adds up what came back from every reaction it belongs to, again weighted by the coefficient, and keeps its own state as well
half 1 hR_r = tanh( Wsr . SUM_i S[i][r] hS_i + Wda da_r + bR )
half 2 hS_i = tanh( Wss . hS_i + Wrs . SUM_r S[i][r] hR_r + bS )
where
hS_i , hR_r
the state each node carries: a vector of length width, six here
S[i][r]
the coefficient on the edge, straight from the matrix
Wsr , Wrs , Wss
the fitted weights, the same ones on every edge and in every voxel
da_r
the Damkohler number of reaction r, an input the edge carries
rounds
how many times the pair above repeats; two in the shipped example

## Slide 4
What happens in one voxel, end to end
Concentrations in, rates out. Nothing is solved and nothing is fitted here; the weights were fixed before the run started.
1
clamp
each concentration is pulled back into the box the fit was made over
C → c
2
scale
each clamped value is mapped linearly onto the interval the fit used
c → x
3
encode
each species node is given its starting state from its own scaled value
x → hS
4
two rounds
the two halves of the previous figure, repeated
hS, hR
5
read out
one number per node, turned into a rate
hS or hR → r
6
units
per_hour divides every rate by 3600
r → R
the shape of each array, for the shipped example

## Slide 5
The two readouts, and why one of them is exact
Step 5 of the previous figure can be taken off the species nodes or off the reaction nodes. That single choice decides whether the rates that come back obey the reaction.
species readout (what a file with no readout line means)
CH4
one number, scaled
SO4
one number, scaled
HS
one number, scaled
HCO3
one number, scaled
four independent numbers. Nothing in the arithmetic ties them together.
extent readout
R1
R2
ξ₁
ξ₂
the four
species rates
r_i = SUM_r S[i][r] * xi_r
one extent per reaction, and the species rates built from the matrix, so their ratios are whatever the matrix says.
the same fit, judged on the one thing the chemistry already fixes
reaction R1 makes one HS for every CH4 it consumes, so this ratio has to be 1
species readout
0.76 to 1.11
extent readout
exactly 1, at every input
0.7
0.8
0.9
1.0
1.1
1.2
HS produced per CH4 consumed
and the fit is no worse for it
species
extent
correlation
0.968
0.972
scaled error
2.21e-2
1.06e-2
stoich residual
n/a
0
fewer output numbers, a slightly
better fit, and a mass balance
that is exact rather than close

## Slide 6
Fitting it offline, and the file it produces
None of this row is inside CompLaB3D. The reader and the writer were checked against each other to machine precision.
a stoichiometry
file
species by reactions
a sample table
one row per condition,
from sweeping the solver
train_graphnet.py
fits the shared weights,
checks the residual
a held-out check
error and correlation on
rows never fitted
write aom.gnn
weights, scalings and
the training box
# CompLaB3D graph network provenance fitted from aom_samples.csv provenance samples 400, R 0.972 provenance stoichiometric residual 0 version 1 units per_hour species CH4 SO4 HS HCO3 reactions R1 rounds 2 width 6 growth 1 readout extent stoich 4 1 -1 -1 1 1 trainmin 2.08e-05 5.20e-05 ... trainmax 4.99e-03 7.93e-03 ... Wenc 0.1198 0.5363 0.6114 ...
where it came from, echoed into the log
the check that the answer respects the matrix
per_hour divides every rate by 3600 on load
THE BINDING: these must be the substrate names of the run
how many rounds of message passing
extent, so the readout is the exact one
the matrix itself, one entry per line
the training box, enforced at every evaluation
the fitted weights
and in CompLaB.xml:
<graphnet>
<enabled>true</enabled>
<network_file>input/aom.gnn</network_file>
</graphnet>
<microbe0>
<reaction_type>graphnet</reaction_type>
...
</microbe0>