## Slide 1
CompLaB3D solve loop: where the thermodynamic gate runs
Model I/O and setup
Flow solver (D3Q19)
Transport solver (D3Q7)
Reaction solver
Mineral solver (VOP)
Load XML configuration
& initialize the simulation conditions
Run flow simulation to steady state
Execute collision step for transport
Abiotic reaction kinetics
Biotic reaction: one rate path per organism
Equilibrium chemistry
Surface reactions on wetted voxels:
precipitation and dissolution
CA biomass expansion
Mineral node update: seal full voxels,
reopen emptied voxels
Pore geometry
changed?
Re-solve steady-state flow field
Yes
No
Streaming step (D3Q7)
& apply boundary conditions
Output save step
reached?
Write output files (VTI)
Yes
No
Max time steps
reached?
No
+ Δt
Yes
End
inside the biotic reaction step, per organism
interchangeable: each takes the local concentrations and
returns a growth rate and the source terms transport needs
compiled kinetics
flux balance analysis (GLPK / COBRApy)
surrogate network
symbolic rate law
graph network
the gate does not replace any of them:
the rate path returns a POTENTIAL rate
the gate returns one number F_T between 0 and 1
the realised rate is the product of the two
computed only in voxels that hold biomass

## Slide 2
One gate, every biotic rate path, one multiplication
Each rate path answers how fast the organism CAN go. The gate answers whether there is enough energy here for it to go at all.
the six biotic rate paths
compiled kinetics
flux balance analysis (GLPK)
flux balance analysis (COBRApy)
surrogate network
symbolic rate law
graph network
each returns a potential rate
the gate
R = R_pot × F_T
the realised rate,
handed to transport
the two abiotic paths
abiotic kinetics
not gated
equilibrium solver
not gated
untouched
what the factor does to a rate
F_T
energy released by the reaction
1
0
the threshold:
m × ΔG_ATP

## Slide 3
F_T is a field, not a number: one value per biomass voxel, every step
There is no single F_T for a run, for a domain or even for an aggregate. The four equations are evaluated again in every voxel that holds biomass, at every reaction step, from that voxel's own concentrations.
a slice of the domain
grains, pore water and four aggregates
solid
open pore
biomass
one aggregate, enlarged
inside one aggregate, at one reaction step
rim
0.55
core 0.06
1
0
F_T
the reaction's own products build up towards the middle, so the free energy available falls and the gate closes from the inside out
how many times it is evaluated
transport
every open voxel
~10.9 million
the rate path
every biomass voxel
~147 thousand
the gate
every biomass voxel
~147 thousand
the gate costs one logarithm and one exponential in about one and a half per cent of the pore volume
the loop, exactly as the solver runs it
for every reaction step:
for every voxel in the domain:
if the voxel holds no biomass: skip it entirely
for every organism in this voxel:
R_pot = the rate path, from THIS voxel's concentrations
F_T = the four equations, from THIS voxel's concentrations
apply R = R_pot * F_T

## Slide 4
The four equations, and one voxel carried down them
Nothing here is iterative and nothing is solved. Four lines of arithmetic, evaluated wherever the previous figure says they are.
this voxel holds: CH4 8.0 mM SO4 12.0 mM HS 0.5 mM HCO3 9.6 mM at 4 °C
1
the reaction quotient
Q = PROD_i a_i ^ nu_i
the four local concentrations,
floored at cmin
Q = 0.0500
2
the free energy actually available
dG = dG0 + R T ln Q + dGloss
dG0, T and dGloss come from
the file, not from the code
dG = − 14.32 kJ/mol
3
what is left after the ATP cost
f = dG + m dG_ATP
m dG_ATP = 0.25 × 50 = 12.5,
the energy threshold
f = − 1.82 kJ/mol
4
the factor that multiplies the rate
F_T = max( 0 , 1 − exp( f / (chi R T) ) )
chi R T = 1 × 2.304 kJ/mol
F_T = 0.547

## Slide 5
The same aggregate, with the gate off and with it on
One switch in the configuration is the only difference. The geometry, the transport coefficients, the metabolic model and the biomass are identical in the two runs.
thermodynamics disabled (the control run)
every voxel runs at the rate its substrates allow, however far the products have built up
the potential rate, voxel by voxel
thermodynamics enabled
the rate falls away towards the middle, where the reaction has spent its own energy
the realised rate, voxel by voxel
what the pair of runs measures
how much slower
the volume average of F_T over the aggregate, which is not F_T evaluated at the bulk composition
where it stopped
the depth into the aggregate at which F_T reaches zero, which no box model can produce
how much bigger it could be
the aggregate radius past which the core contributes nothing, which is a size limit the model derives rather than assumes

## Slide 6
The energetics file, line by line
One switch and one file name live in CompLaB.xml. Every number that decides where the gate closes is here, in something a reader can open, diff and cite.
# aom.thm provenance dG0 from He et al. (2021) version 1 temperature 277.15 energy_units kJ concentration_scale 1 reaction AOM microbe ANME stoich CH4 -1 SO4 -1 HS 1 HCO3 1 dG0 -33.12 atp 0.25 dGatp 50.0 chi 1.0 cmin 1e-9 dGloss 25.7 yield on dGana -30.0 carbon 1 reduction 8.0 yieldmax 0.05
where the numbers came from; echoed into the log
the temperature dG0 is quoted at, in kelvin
one block per reaction; the name is for the log
which organism, by name from the configuration
negative consumed, positive produced; an unknown name is a hard error
the standard free energy, at the temperature above
ATP per turnover and the energy of one ATP;
their product 12.5 kJ/mol is the threshold
average stoichiometric number; one unless measured
activity floor, so ln Q stays finite at zero
electron transfer loss, added to dG so it reduces
what is available; 0 recovers direct contact
the growth yield block, off by default
the whole of the configuration side:
<thermodynamics>
<enabled>true</enabled>
<energetics_file>input/aom.thm</energetics_file>
</thermodynamics>

## Slide 7
The optional growth yield, and why it is off by default
With the yield off, the gate only scales a rate. With it on, the same free energy also says how much biomass one turnover of the reaction buys.
the carbon source
NoC and degree of reduction
the Heijnen and van Dijken
dissipation correlation
ΔG_dis
kJ per C-mol
dG_dis = 200 + 18 (6 - NoC)^1.8 + exp[ ((3.8 - gamma)^2)^0.16 (3.6 + 0.4 NoC) ]
Y = ΔG / −( ΔG_ana + ΔG_dis )
C-mol biomass per mole of reaction
the same ΔG the gate computed one line earlier